- PLEASE NOTE THAT ON A QUAD AXLE TRAILER, THERE IS ONE ADDITIONAL FRONT EQUALIZER BETWEEN THE FRONT AND SECOND AXLE AND THEN FROM THE SECOND BACK TO THE FOURTH AXLE SHOULD LOOK JUST LIKE THE TRI AXLE SET UP AS SHOWN ABOVE

- WITH THE SPRING AXLE SUSPENSION, THIS IS HOW YOUR SPRINGS AND EQUALIZERS SHOULD LOOK.  PLEASE NOTE THAT THE EQUALIZERS MAY NOT ALWAYS BE COMPLETELY LEVEL, BUT THE SPRINGS SHOULD ALWAYS BE ON TOP OF THE EQUALIZERS.  ON THE BACK OF THE FRONT EQUALIZER THE SPRING CAN NOT MOVE SO THIS IS OF NO ISSUE.  IF YOUR SUSPENSION EVER DOES NOT RESEMBLE THIS PLEASE CALL LOADMASTER FOR A REMEDY.

- CAUTION:  IF THE SPRING AT ANY ONE OF THE EQUALIZERS IS BELOW THE EQUALIZER THE AXLE HAS “FLIPPED”.  DO NOT TOW THE TRAILER WITH ANY WEIGHT ON IT.  THE AXLE CAN BE DAMAGED AND THE TRAILER COULD SWAY UNCONTROLLABLY. CALL LOADMASTER FOR A REMEDY TO THE SITUATION.